Kinematics for Lynxmotion Robot Arm
Dr. Rainer Hessmer, October 2009

Note: This article contains text and two graphics from the reference [1] listed at the end.
# Kinematics
## Forward Kinematics
Given the joint angles and the links geometry, compute the orientation of the end effector relative to the base frame.
## Inverse Kinematics
Given the position and orientation of the end effector relative to the base frame compute all possible sets of joint angles and link geometries which could be used to attain the given position and orientation of the end effector.

# 2R Planar Manipulator

Figure 1: Elbow up (a) and Elbow down (b) configuration of a 2R planar manipulator

## Forward Kinematics
alignl x `=` l_1 cos %theta_1 `+` l_2 cos(%theta_1 + %theta_2) newline newline alignl y `=` l_1 sin %theta_1 `+` l_2 sin(%theta_1 + %theta_2)

## Inverse Kinematics
x^2 + y^2 `=` l_1^2 cos^2 %theta_1 `+` l_2^2 cos^2(%theta_1 + %theta_2) `+` 2 l_1 l_2 cos %theta_1 cos(%theta_1 + %theta_2) `+` newline ~~~~~l_1^2 sin^2 %theta_1 `+` l_2^2 sin^2(%theta_1 + %theta_2) `+` 2 l_1 l_2 sin %theta_1 sin(%theta_1 + %theta_2) newline newline alignl ~~~~~~`` `=` l_1^2 `+` l_2^2 `+` 2 l_1 l_2 [ cos %theta_1 cos(%theta_1 + %theta_2) `+` sin %theta_1 sin(%theta_1 + %theta_2)]

Next we use the following equalities:

sin(x+-y) `=` sin x cos y `+-` cos x sin y newline alignl cos(x+-y) `=` cos x cos y `-+` sin x sin y

Therefore

x^2 + y^2 `=` l_1^2 `+` l_2^2 `+` 2 l_1 l_2 [ cos %theta_1 ( cos %theta_1 cos %theta_2 - sin %theta_1 sin %theta_2) `+` sin %theta_1 ( sin %theta_1 cos %theta_2 + cos %theta_1 sin %theta_2)] newline newline alignl ~~~~~~`` `=` l_1^2 `+` l_2^2 `+` 2 l_1 l_2 [ cos^2 %theta_1 cos %theta_2 `+` sin^2 %theta_2 cos %theta_2 ] newline newline alignl ~~~~~~`` `=` l_1^2 `+` l_2^2 `+` 2 l_1 l_2 cos %theta_2

and

cos %theta_2 `=` {x^2 + y^2 - l_1^2 - l_2^2} over { 2 l_1 l_2}

From here we could get the angle directly using the arccose function but this function is very inaccurate for small angles. The typical way to avoid this inaccuracy is to convert further until we can use the atan2 function.

cos^2 %theta_2 + sin^2 %theta_2 `=` 1 newline newline sin %theta_2 `=` +- sqrt{1 - cos^2 %theta_2}

The two solutions correspond to the 'elbow up' and 'elbow down' configurations as shown in figure 1 a) and b).

Finally we get:

alignl %theta_2 ~=~ atan2(sin %theta_2, cos %theta_2) ~=~ newline newline alignl ~~~~~~` atan2(+- sqrt{1 - cos^2 %theta_2}, cos %theta_2) ~=~ newline newline alignl ~~~~~~` atan2(+- sqrt{1 - ({x^2 + y^2 - l_1^2 - l_2^2} over { 2 l_1 l_2})^2} , {x^2 + y^2 - l_1^2 - l_2^2} over { 2 l_1 l_2} )

For solving %theta_1 we rewrite the original nonlinear equations using a change of variables as follows (see figure 2):

alignl x `=` l_1 cos %theta_1 `+` l_2 cos(%theta_1 + %theta_2) newline newline alignl y `=` l_1 sin %theta_1 `+` l_2 sin(%theta_1 + %theta_2) newline newline newline alignl x `=` k_1 cos %theta_1 `-` k_2 sin %theta_1 newline newline alignl y `=` k_1 sin %theta_1 `+` k_2 cos %theta_1

where

alignl k_1 `=` l_1 + l_2 cos %theta_2 newline newline alignl k_2 `=` l_2 sin %theta_2
Figure 2 (taken from [1])

Next we change the way we write the constants k_1, k_2 (see figure 3)

alignl r `=` sqrt{k_1 ^2 + k_2 ^ 2} newline newline alignl %gamma = atan2(k_2, k_1) newline newline newline alignl k_1 `=` r cos %gamma newline newline alignl k_2 `=` r sin %gamma

Figure 3 (taken from [1])

Inserting into the previous transformations of x and y yields:

alignl x `=` r cos %gamma cos %theta_1 `-` r sin %gamma sin %theta_1 newline newline alignl y `=` r cos %gamma sin %theta_1 `+` r sin %gamma cos %theta_1

or

alignl x over r `=` cos %gamma cos %theta_1 `-` sin %gamma sin %theta_1 newline newline alignl y over r `=` cos %gamma sin %theta_1 `+` sin %gamma cos %theta_1

or

alignl x over r `=` cos (%gamma + %theta_1) newline newline alignl y over r `=` sin (%gamma + %theta_1)

Applying the atan2 function:

alignl %gamma + %theta_1 atan2(y over r, y over r) `=` atan2(y,x) newline newline alignl %theta_1 `=` atan2(y,x) - atan2(k_2, k_1)

where

alignl k_1 `=` l_1 + l_2 cos %theta_2 newline newline alignl k_2 `=` l_2 sin %theta_2

Notes
- Switching to another choice of sign in the solution for %theta_2 above will change the sign of %k_2 and thus will affect %theta_1 .
- If x = y = 0 then the solution becomes undefined. In this case %theta_1 is arbitrary. Note that this is only possible if both links have the same length and can fold back onto each other.

# Inverse Kinematics for Lynxmotion Robot Arm
Here we focus on the inverse kinematics for the wrist without taking the gripper into account. This means the robot arm can be described as a 2R planar manipulator on a rotating base.

Figure 4: Side view of Lynxmotion robot arm without gripper.

Figure 5: Top view of Lynxmotion robot arm without gripper.

The goal is to calculate the angles %theta_0, %theta_1, %theta_2 from the position (x,y,z) of the wrist. Note that the x,y,z axes as illustrated in figures 4 and 5 do not match the default coordinate system used by the RIOS software.

The angle %theta_0 is fully defined by the coordinates x and y:

%theta_0 `=` atan2(y,x)

In order to get the other two angles we leverage the distance d of the point (x,y) from the origin and the height z' above the shoulder joint.
alignl d `=` sqrt{x^2 + y^2} newline newline alignl z' `=` z - b
where b is the height of the shoulder joint (see figure 4 for details).

This allows us to use the calculations for the 2R planar manipulator. d is plugged in as the x value into the formulas for %theta_1 and %theta_2 and z' is used in as the y value.

## References
- [1] MECH 498: Introduction to Robotics, Inverse Manipulator Kinematics
  by M. O’Malley
  http://www.owlnet.rice.edu/~mech498/498lecture4.pdf
- [2] Stanford University Course: Artificial Intelligence | Introduction to Robotics
  by Khatib, Oussama
  (http://see.stanford.edu/see/courseInfo.aspx?coll=86cc8662-f6e4-43c3-a1be-b30d1d179743)
- [3] Theory of Applied Robotics: Kinematics, Dynamics, and Control
  by Resa N. Jazar
  (http://www.amazon.com/Theory-Applied-Robotics-Kinematics-Dynamics/dp/0387324755/ref=sr_1_1?ie=UTF8&s=books&qid=1255828006&sr=8-1)